## Slide 1: DigitalBin
Simone aresta
francesco pietri
Notes: Francesco

## Slide 2: Main Goals
Urban and rural upkeep
Preventing bin overflows
Enhanced schedule of waste collectors
Enhance maintenance interventions
Notes: Francesco

## Slide 3: Infrastructure Overview
10km
HiveMQ public
MQTT Broker
Central Controller
Public Thingsboard CE instance
Notes: Francesco

## Slide 4: 1. Digital Bin
The Digital Bin sends
Once, its geographical coordinates (lat and lon)
It periodically sends the fill level and overturn status (yes/no)
Notes: Simone

## Slide 5: 2. Receiver LoRa + Bridge
Receiver LoRa receives data from the Digital Bins in the area and send them to the Bridge
Bridge forwards the data on a MQTT Server and takes the data from it
Notes: Simone

## Slide 6: 3. Central Controller
It is the brain of the project. It is responsible for processing the data.
It communicates when to close the bins
It notifies when the bins are overturned
If a bin is closed, it calculates the distance to the nearest free bin.
It sends the updates to the web dashboard
Notes: Simone

## Slide 7: 4. Web Dashboard
It exploits ThingsBoard CE
It shows map on where the bins are located
It shows fill level of each bin
It shows a chart displaying the fill level of each bin over time
You can ask to a ML Model the fill level of a bin in the future
Notes: Simone

## Slide 8: Digital Bin In Depth
Notes: Francesco

## Slide 9: DigitalBin – Onboard Hardware
Microcontroller
Magnetometer, Accelerometer,
Gyroscope
Display
LoRa radio
transmitter
NFC card reader
Ultrasonic
sensor
STD Servo motor
BMO055
SSD1306
HC-SR04
SX1278
RFID - RC522
Arduino Mega 2560​
Notes: Francesco

## Slide 10: DigitalBin – Receiver Hardware
Microcontroller
Arduino Uno
Bridge Computer
LoRa radio
transmitter
SX1278
Notes: Francesco

## Slide 11: DigitalBin - LoRa Technology
LoRa (Long Range) is a radio modulation technique used to create long-range (5-10 km) communication links.
The communication is Broadcast (433 Mhz)
It’s designed for low power usage and low bandwidth (sending small data packets)
For the project, LoRa is used to connect more digital bins with a central receiver. Each digital bin sends data of its sensors to the receiver, and the receiver sends the information of what to do (created by Central Controller) to each digital bin.
Notes: Francesco

## Slide 12: DigitalBin – Packet (Bin → Bridge)
START_SEQ
POSITION/FILL/OVERTURN
ID
PAYLOAD
PAYLOAD
Position → lat,lon
Fill → fill_level (%)
Overturn → is_Overturn (true/false)
Notes: Simone

## Slide 13: DigitalBin – Packet (Bridge → Bin)
START_SEQ
CMD
CMD_LOCK
CMD_LCD
MY_ADDRESS
START_MARKER
0xFE
CMD
PAYLOAD
END_MARKER
0xFF
FSM
Notes: Simone

## Slide 14: DigitalBin - Finite State Machine
FSM - Mealy
Notes: Simone

## Slide 15: Receiver LoRa
The goal of this component is to connect the Digital Bins with the Bridge.
Bin → Bridge: it listens via LoRa. When it receives the packet, it forwards that on the Bridge
Bridge → Bin: it listens via Serial. When it receives the packet (0xFE … 0xFF), it packs that, inserting the start_seq and the address of destination digital_bin
Notes: Francesco

## Slide 16: Receiver LoRa - Acknowledgment
Receiver LoRa
Digital Bin
Create Packet
Compute CRC
Receive Packet
Compute CRC
Send it as ACK
Waiting
For Ack
Compare CRC
If Equal ✔
Otherwise send again
(3 times max)
Notes: Francesco

## Slide 17: Bridge
The Bridge has the role to connect the Digital Bins to the digital real world. In particular it converts the data from Serial (used to communicate with Receiver LoRa) to MQTT (TCP/IP) (used to communicate with HiveMQ) and viceversa
The Bridge is Publisher for
/Bins/Bin_id/fill
/Bins/Bin_id/overturn
/Bins/Bin_id/position
The Bridge is Subscriber for
/Bins/Bin_id/lock
/Bins/Bin_id/lcd
Notes: Francesco

## Slide 18: HiveMQ
HiveMQ is a fully managed MQTT Cloud Platform that aim to create reliable, scalable and secure MQTT cloud-broker clusters that are built for production. The free tier allows to connect up to 100 devices and gives 10Gb of MQTT traffic each month.
In our architecture we use it to transfer data from periferal bin to the central controller.
Notes: Francesco

## Slide 19: Central Controller
Subscribe to:
Fill
Overturn
Position
Data is stored in Json files and dictionaries
The Controller decide:
When to close the lid
Compute the direction and distance of the next free bin
Predictive modeling of bin saturation based on past collection cycles.
Upload data to a ThingsBoard dashboard for visualization.
Publish on:
Lock
lcd
Notes: Francesco

## Slide 20: Central Controller - Next open bin detection
1km
The controller checks for the presence of other bins within a 1km radius. If multiple bins are detected, it selects the nearest one.
The new bin must be open.
Utilizing an onboard sensconsisting of a magnetometer, accelerometer, and gyroscope, the bin maintains full 3D orientation awareness. This enables the system to perform dynamic heading compensation, ensuring the directional arrow remains accurate even when the device is rotated
Notes: Francesco

## Slide 21: Central Controller - ML Predictor Pipeline
Takes Data
Cleaning Data:
Outliers detection
Missing value
Features exctractor
Cyclical Encoding
Storage Data
Json file
Train Model
Prediction
Notes: Simone

## Slide 22: Thingsboard
Thingsboard is an open-source IoT (Internet of Things) platform designed for data collection, processing, visualization, and device management.
In particular we use it in our project as an interactive dashboard that waste collectors can use to check the bin state and location.
Self-hosted thingsboard instance
Central Controller
MQTT Protocol
Data is sent to a gateway via the MQTT protocol. The gateway is responsible for dynamically provisioning new devices and forwarding the relevant telemetry to them. This data is then used to generate real-time graphs and visualizations within the dashboard
Notes: Francesco

## Slide 23: Waste Collector - Interactions
The Waste Collector can interact with the system by the
Web Dashboard (ThingsBoard)
NFC Module
Notes: Simone

## Slide 24: Waste Collector - NFC
The NFC Module allows authorized personal to open a full bin to empty it.
Emptying
, Enter configuration mode
Exit configuration mode
Notes: Simone

## Slide 25: Waste Collector - Dashboard
Each waste collector has a customer account within Thingsboard
Notes: Francesco

## Slide 26: Waste Collector - Dashboard
Administrators centrally manage collectors by assigning specific assets and dashboards. This regulates access and permissions, significantly enhancing security through organized emploee management
Notes: Francesco

## Slide 27: Pro and Cons
Pro:
Cheap hardware and installation
Low consumption and long range thanks to LoRa
Software easy to extend thanks to the modular approch
Software easy to develop thanks to python
No need for subscription plan to external service
Easy and centralized emploee management
Cons:
Might need to upgrade HiveMQ plan for higher trasmission limits
Low responsivness due LoRa regulation , teoretically 1 trasmission every 3/4 mins
Notes: Francesco

## Slide 28: Future developments
Notes: Simone

## Slide 29: Future Developments
Integrate a real Machine Learning model such as Prophet or Random Forest
Enhance the hardware by implementing an IP-rated waterproof enclosure, a rain-activated automatic closure system, and an integrated GPS module for precise geolocation.
Notes: Simone

## Slide 30: Future Developments
Improve waste collector schedule and route based on distance and forecasting prediction
Upgrade the dashboard to enable waste collectors to report specific maintenance or operational problems
Notes: Simone

## Slide 31: Thanks for your attention
By Francesco Pietri, Simone Aresta